## Slide 1: Internship Reporting
STUDENT:
Oriol CHANDRE VILA
TUTORS:
Joseph MORLIER (ISAE-SUPAERO) and Sylvain DUBREUIL (ONERA)
ONERA, Toulouse
Summer 2018

## Slide 2: Table of Contents
Introduction
Aim and Objectives
State of the Art
Results
Future work
Internship Reporting | Oriol CHANDRE VILA

## Slide 3
Introduction
Aeroelasticity
Coupling between aerodynamic forces, inertial forces and elastic forces.
Current issues due to models dimension. Why the ROM?
The calculations have a high cost in time and computational power.
Mean vorticity field
[Kutz et al., Chpt 9, SIAM, 2016]
[Kutz et al., Chpt 9, SIAM, 2016)
Internship Reporting | Oriol CHANDRE VILA

## Slide 4
Aim & Objectives
Aim
To implement an approach Greedy+POD to an aeroelastic code in order to lighten the further simulations.
Objectives
To apply the abovementioned technique to the proposed problem.
To analyse the results.
Source [5]
Internship Reporting | Oriol CHANDRE VILA

## Slide 5
State of the Art
Principal Component Analysis (PCA)
Widely used in the actuality.
Limitations:
  The results depend on the scaling variables.
  The applicability is limited by certain assumptions.
  No differentiation between classes.
Used in different disciplines:
  SVD in Algebra
  POD in Mechanical Engineering.
Possible correlated variables
(Observations)
Orthogonal Transformation
Values of linearly uncorrelated variables
(Principal Components)
SVD approach:
In Matlab:
[U,S,V] = svd(A)
[Ar] = U(:,1:k)*S(1:k,1:k)*V(:,1:k)’
[Kutz, Chpt 15, Oxford University Press, 2013]
Internship Reporting | Oriol CHANDRE VILA

## Slide 6
Results
  Aero structure problem
Internship Reporting | Oriol CHANDRE VILA
Aerodynamics  VLM Horseshoe
Matrix of Transfer & Mesh deformation
Structures  FEM (DKT for plates)
6 parameters of interest
Span
Wing Area
Source [5]

## Slide 7
Results
  Aero structure problem
Algorithm Greedy POD - OFFLINE
Select randomly a first sample:
Solve the HDM:
Build a corresponding ROB:
For i = 2 ,, nSample
  Solve:
  Solve the HDM:
  Build a ROB based on the samples
[Amsallem, International Journal for Numerical Methods in Engineering, 2014]
V size:
Circulation: 627 x nSamples
Displacement: 2988 x nSamples
Internship Reporting | Oriol CHANDRE VILA
KRIGING: nSamples functions
Approximation ONLINE
[Wahba et al., SIAM, 1990]

## Slide 8
Results
  Aero structure problem
Internship Reporting | Oriol CHANDRE VILA
nSamples = 15 // nCandidates = 30
= 0,03 m
= 0,01 m
= 0,022 m
= 0,011 m
b = 73,20 m
S = 444,44

## Slide 9
Results
  Aero structure problem
Internship Reporting | Oriol CHANDRE VILA

## Slide 10
Results
  Aero structure problem
Internship Reporting | Oriol CHANDRE VILA

## Slide 11
Conclusions and Future work
CONCLUSIONS
Saving computation time in a real time simulation.
nSamples drives the accuracy of the RB.
Kriging procedure  acceptable variance values
In displacement approximation  real solution is not localized between the limits
FUTURE WORK?
Introduction of the reduced base methodology to the solver OpenAeroStruct.
Internship Reporting | Oriol CHANDRE VILA
Link to the GitHub Project

## Slide 12
References
[1] Kutz, J.N., Brunton, S.L., Brunton, B.W. and Proctor, J.L., "Dynamic Mode Decomposition: Data-Driven Modeling of Complex Systems", 1st ed., SIAM, Philadelphia, 2016.
[2] Kutz, J. N., "Data-Driven Modeling & Scientific Computation: Methods for Complex Systems & Big Data", 1st ed., Oxford University Press, Oxford, 2013.
[3] Amsallem, D., “An Adaptive and Efficient Greedy Procedure for the Optimal Training of Parametric Reduced-Order Models”, International Journal for Numerical Methods in Engineering, 2014.
[4] Wahba, G., "Spline Models for Observational Data", Society for Industrial and Applied Mathematics (SIAM), 1990.
[5] http://www.dlr.de/ae/en/desktopdefault.aspx/tabid-1596/
[6] http://www.lissys.demon.co.uk/pug/c03.html
Internship Reporting | Oriol CHANDRE VILA